## Slide 1: CMSIS: Cortex Microcontroller Software Interface Standard

## Slide 2: Overview
What is CMSIS?
  Hardware Abstraction Layer: Layer of software between application program and hardware
  Conventions and standards for software interfaces, structure and names
Problem – too many options
  Some Cortex-M architectures offer additional instructions
    When targeting Cortex-M4, compiler has additional instructions available (e.g. floating point, SIMD) compared with M0+
  Many MCU vendors create Cortex-M-based MCUs
    Although CPU cores are consistent, peripherals are structured and accessed differently
  Many compilers available
    Different approaches to implementing features not defined in C/C++ specifications
  Many RTOSs available
    Different APIs
Benefits
  Shortens learning curve on new hardware
  Simplifies software development
  Simplifies software reuse

## Slide 3: CMSIS Structure
Detailed documentation available through MDK: Help->Open Books Window, then select Tool User’s Guide-> CMSIS Documentation
Notes: One major benefit of CMSIS is that it standardizes the structure and interfaces between the components shown here, enabling interoperability and simplifying development.

## Slide 4: Conventions
General
  Compliant with ANSI C and C++
  Uses ANSI C <stdint.h> data types
  Conforms to MISRA 2004
Naming conventions
  CAPITAL names for core registers, peripheral registers, CPU instructions
  CamelCase for function and interrupt function names
  Namespace_ prefixes to group and isolate functional groups
Documentation
  Doxygen-compliant function comments with function overview, detailed description, parameter explanation, return value information
Licensing
  Free of charge
  Can be used for all Cortex-M-based devices

## Slide 5: CMSIS-CORE
CMSIS-CORE device files (blue) implement device-specific functionality
User application includes <device.h> to use CMSIS-CORE features
  Peripheral access
  Interrupts and exceptions
  Intrinsic CPU functions
  Systick timer
  Debug Access for printf-style I/O
Additional features
  Standard API for Cortex-M processor core and peripherals
  Header file organization and naming conventions
  System initialization function skeletons, implemented by MCU vendors
  Support for determining system clock frequency

## Slide 6: Example: Accessing Hardware Registers in C
Header file MKL25Z4.h
  Defines C data structure types to represent MCU hardware registers
/** GPIO - Register Layout Typedef */
typedef struct {
__IO uint32_t PDOR; /**< Port Data Output Register, offset: 0x0 */
__O uint32_t PSOR; /**< Port Set Output Register, offset: 0x4 */
__O uint32_t PCOR; /**< Port Clear Output Register, offset: 0x8 */
__O uint32_t PTOR; /**< Port Toggle Output Register, offset: 0xC */
__I uint32_t PDIR; /**< Port Data Input Register, offset: 0x10 */
__IO uint32_t PDDR; /**< Port Data Direction Register, offset: 0x14 */
} GPIO_Type;

## Slide 7: Example: Accessing Hardware Registers in C
Header file MKL25Z4.h
  Declares pointers to the registers
/* GPIO - Peripheral instance base addresses */
/** Peripheral PTA base address */
#define PTA_BASE (0x400FF000u)
/** Peripheral PTA base pointer */
#define PTA ((GPIO_Type *)PTA_BASE)
PTA->PDOR = my_data;

## Slide 8: Example: Using The Ports
#include <MKL25Z4.h>
#define LED1_POS (1)
#define LED2_POS (2)
#define SW1_POS (5)
#define MASK(x) (1UL << (x))
PTA->PDDR |= MASK(LED1_POS) | MASK(LED2_POS); // set bits to outputs
PTA->PDDR &= ~MASK(SW1_POS); // clear switch bit to input
PTA->PDOR = MASK(LED2_POS); // turn on LED1, turn off LED2
while (1) {
if (PTA->PDIR & MASK(SW1_POS)) { // switch is not pressed, so light LED 2
PTA->PDOR = MASK(LED2_POS);
} else { // switch is pressed, so light LED 1
PTA->PDOR = MASK(LED1_POS);
}
}
Notes: Here we see how to use CMSIS to access port A for GPIO.

## Slide 9: CMSIS-Driver
Software API for peripheral driver interfaces
Generic and RTOS-independent
Covers typical use cases for common peripherals
Example functions for USART
  ARM_USART_Control: configure communication parameters
  ARM_USART_PowerControl: control USART power mode
  ARM_USART_Send: Start to send data in buffer
  ARM_USART_Receive: Start to receive data into buffer
  ARM_USART_SignalEvent: callback function to notify application when event occurs (e.g. transmission complete)
  ARM_USART_GetTxCount: Return number of items which have been sent
  etc.

## Slide 10: CMSIS-DAP
Cortex-M MCUs have built-in debug support (CoreSight), accessible via Debug Access Port
Use a debug MCU to translate between USB (for PC communications) and target MCU (with JTAG or SW interface)
CMSIS-DAP is standardized firmware for this debug MCU
USB
Target MCU
Debug MCU running CMSIS-DAP firmware

## Slide 11: CMSIS-DSP Software Library
Library of fast functions and macros for digital signal processing, other math
  Basic math – abs, add, sub, multiply, negate, offset, scale, shift (all support vector operations)
  Fast math – sin, cos, sqrt
  Complex math
  Filters – IIR, FIR, convolution, correlation, FIR LMS, interpolator
  Matrix
  Transforms – FFT, DCT
  Motor control – PID control, Clarke & Park (and inverse) transforms
  Statistical – min, max, mean, power, rms, standard deviation, variance
  Support – vector fill & copy, convert values
  Interpolation – linear, bilinear
Multiple data types supported
  32-bit floating point
  32-bit integer/fixed point
  16-bit integer/fixed point
  8-bit integer/fixed point
Different versions optimized for Cortex M versions
  M0, M0+, M3, M4
Detailed documentation available through MDK: Help->Open Books Window, then select Tool User’s Guide-> CMSIS Documentation

## Slide 12: CMSIS-DSP Support for Fixed Point Math
Three fractional fixed point data types supported
  q31_t: signed, 1 integer bit, 31 fraction bits
  q15_t: signed, 1 integer bit, 15 fraction bits
  q7_t: signed, 1 integer bit, 7 fraction bits. Not supported by all functions.
Fractional: range is -1 to +1
To use CMSIS-DSP library
  #include <arm_math.h>
  C/C++ Tab: Define preprocessor symbol ARM_MATH_CM0PLUS
  Linker Tab: Specify ARM math library to use, with location

## Slide 13: Example Code – Pythagorean Theorem
Equivalent C code
  c = sqrtf((a*a) + (b*b));
To use fixed point functions, we need to break expression into individual operations
  a_2 = a*a;
  b_2 = b*b;
  sum = a_2 + b_2;
  c = sqrtf(sum);
Note that not all arguments are passed as pointers

## Slide 14: CMSIS-RTOS API
Defines a generic RTOS interface
  Provides minimum feature set
  May be extended by RTOS vendors
Core Functionality
  Kernel information and control
  Thread management
  Event management: signals, message queues, mail queues
  Mutex and semaphore management
  Wait functions
  Timer management
  Memory pool management

## Slide 15: Other CMSIS Components
CMSIS-Pack
  Delivery mechanism and format for …
    Software components
    Device parameters
    Evaluation board support
CMSIS-SVD
  System View Description format
    Developed by MCU vendor
    Provides formal description of programmer’s view of system (e.g. memory-mapped registers) in MCU
    Detailed information similar to reference manual – register names, bit field names, values and functionality
    Used to generate CMSIS-compliant device header files