## Slide 1: Analog Interfacing

## Slide 2: Why It’s Needed
Embedded systems often need to measure values of physical parameters
These parameters are usually continuous (analog) and not in a digital form which computers (which operate on discrete data values) can process
Pressure
  Blood pressure monitor
  Altimeter
  Car engine controller
  Scuba dive computer
  Tsunami detector
Acceleration
  Air bag controller
  Vehicle stability
  Video game remote
Mechanical strain
Other
  Touch screen controller
  EKG, EEG
  Breathalyzer
Temperature
  Thermometer (do you have a fever?)
  Thermostat for building, fridge, freezer
  Car engine controller
  Chemical reaction monitor
  Safety (e.g. microprocessor processor thermal management)
Light (or infrared or ultraviolet) intensity
  Digital camera
  IR remote control receiver
  Tanning bed
  UV monitor
Rotary position
  Wind gauge
  Knobs

## Slide 3: Converting Between Analog and Digital Values

## Slide 4: The Big Picture – A Depth Gauge
Sensor detects water pressure and generates a proportional output voltage V_sensor
ADC generates a proportional digital integer (code) based on V_sensor and V_ref
Code can convert that integer to a something more useful
  first a float representing the voltage,
  then another float representing pressure,
  finally another float representing depth
Pressure Sensor
Analog to Digital Converter
// Your software
ADC_Code = ADC0->R[0];
V_sensor = ADC_code*V_ref/1023;
Pressure_kPa = 250 * (V_sensor/V_supply+0.04);
Depth_ft = 33 * (Pressure_kPa –
Atmos_Press_kPa)/101.3;
V_sensor
ADC_Code
V_ref
V_sensor
ADC_Code
Voltages
V_ref
Ground
ADC Output Codes
111..111
000..000
000..001
111..110
111..101
111..100
Water Pressure
Notes: Let’s take a look at how an electronic depth gauge on a scuba diver or submarine works using an analog to digital converter.

## Slide 5: Getting From Analog to Digital
A Comparator tells us “Is Vin > Vref?”
  Compares an analog input voltage with an analog reference voltage and determines which is larger, returning a 1-bit number
  E.g. Indicate if depth > 100 ft
  Set Vref to voltage pressure sensor returns with 100 ft depth.
An Analog to Digital converter [AD or ADC] tells us how large Vin is as a fraction of Vref.
  Reads an analog input signal (usually a voltage) and produces a corresponding multi-bit number at the output.
  E.g. calculate the depth
0
Vin
Vref
Comparator
0
1
0
1
Vin
Vref
Clock
A/D Converter
Notes: There are two common devices used to convert from analog to digital. The comparator gives a simple Higher/Lower answer, while the ADC gives a proportional digital value.

## Slide 6: Digital to Analog Conversion
May need to generate an analog voltage or current as an output signal
  E.g. audio signal, video signal brightness.
DAC: “Generate the analog voltage which is this fraction of Vref”
Digital to Analog Converter equation
  n = input code
  N = number of bits of resolution of converter
  Vref = reference voltage
  Vout = output voltage. Either
    Vout = Vref * n/(2N) or
    Vout = Vref * (n+1)/(2N)
    The offset +1 term depends on the internal tap configuration of the DAC – check the datasheet to be sure
0
1
0
1
Vout
Vref
D/A Converter

## Slide 7: Waveform Sampling and Quantization
A waveform is sampled at a constant rate – every Dt
  Each such sample represents the instantaneous amplitude at the instant of sampling
  “At 37 ms, the input is 1.91341914513451451234311… V”
  Sampling converts a continuous time signal to a discrete time signal
The sample can now be quantized (converted) into a digital value
  Quantization represents a continuous (analog) value with the closest discrete (digital) value
  “The sampled input voltage of 1.91341914513451451234311… V is best represented by the code 0x018, since it is in the range of 1.901 to 1.9980 V which corresponds to code 0x018.”
time
Digital value

## Slide 8: Forward Transfer Function Equations
General Equation
n = converted code
Vin = sampled input voltage
V+ref = upper voltage reference
V-ref = lower voltage reference
N = number of bits of resolution in ADC
(
)
2
/
1
2
ú
ú
û
ê
ê
ë
+
-
-
=
-
+
-
ref
ref
N
ref
in
V
V
V
V
n
(
)
2
/
1
2
ú
ú
û
ê
ê
ë
+
=
+
ref
N
in
V
V
n
676
2
/
1
5
2
30
.
3
10
=
ú
û
ê
ë
+
=
v
v
n
Simplification with V-ref = 0 V
û
ë
floor function: nearest integer I such that I <= X
floor(x+0.5) rounds x to the nearest integer
X = I
What code n will the ADC use to represent voltage Vin?

## Slide 9: Inverse Transfer Function
General Equation
n = converted code
Vin_min = minimum input voltage for code n
Vin_max = maximum input voltage for code n
V+ref = upper voltage reference
V-ref = lower voltage reference
N = number of bits of resolution in ADC
Simplification with V-ref = 0 V
What range of voltages Vin_min to Vin_max does code n represent?

## Slide 10: What if the Reference Voltage is not known?
Example - running off an unregulated battery (to save power)
Measure a known voltage and an unknown voltage
Many MCUs include an internal fixed voltage source which ADC can measure for this purpose
Can also solve for Vref
  “My ADC tells me that channel 27 returns a code of 0x6543, so I can calculate that VREFSH = 1.0V * 216/0x6543 = …

## Slide 11: Analog to Digital conversion concepts

## Slide 12: A/D – Flash Conversion
A multi-level voltage divider is used to set voltage levels over the complete range of conversion.
A comparator is used at each level to determine whether the voltage is lower or higher than the level.
The series of comparator outputs are encoded to a binary number in digital logic (a priority encoder)
Components used
  2N resistors
  2N-1 comparators
Note
  This particular resistor divider generates voltages which are not offset by ½ bit, so maximum error is 1 bit
  We could change this offset voltage by using resistors of values R, 2R, 2R ... 2R, 3R (starting at bottom)
1/8 V
2/8 V
3/8 V
4/8 V
5/8 V
6/8 V
7/8 V
+
-
Encoder
+
-
+
-
+
-
+
-
+
-
+
-
1V
V
in
Comparators
R
R
R
R
R
R
R
R
3
1
1
1
0
0
0
0

## Slide 13: ADC - Successive Approximation Conversion
Successively approximate input voltage by using a binary search and a DAC
SA Register holds current approximation of result
Set all DAC input bits to 0
Start with DAC’s most significant bit
Repeat
  Set next input bit for DAC to 1
  Wait for DAC and comparator to stabilize
  If the DAC output (test voltage) is smaller than the input then set the current bit to 1, else clear the current bit to 0
Voltage
Time
Start of
Conversion
Test voltage (DAC output)
T
1
T
2
T
3
T
4
T
5
T
6
000000
111111
100000
100100
Analog Input
know 1xxxxx, try 110000
100110
know xxxxxx, try 100000
know 10xxxx, try 101000
know 100xxx, try 100100
know 1001xx, try 100110
know 10011x, try 100111
know 100110. Done.

## Slide 14: A/D - Successive Approximation
Converter Schematic
Notes: The hardware for the successive approximation ADC uses a comparator to compare the input voltage against a test voltage generated by the D/A converter, which is driven by the successive approximation register according to the sequence on the previous slide.

## Slide 15: ADC Performance Metrics
Linearity measures how well the transition voltages lie on a straight line.
Differential linearity measure the equality of the step size.
Conversion time: between start of conversion and generation of result
Conversion rate = inverse of conversion time

## Slide 16: Sampling Problems
Nyquist criterion
  Fsample >= 2 * Fmax frequency component
  Frequency components above ½ Fsample are aliased, distort measured signal
Nyquist and the real world
  This theorem assumes we have a perfect filter with “brick wall” roll-off
  Real world filters have more gentle roll-off
  Inexpensive filters are even worse (e.g. first order filter is 20 dB/decade, aka 6 dB/octave)
  So we have to choose a sampling frequency high enough that our filter attenuates aliasing components adequately

## Slide 17: Inputs
Differential
  Use two channels, and compute difference between them
  Very good noise immunity
  Some sensors offer differential outputs (e.g. Wheatstone Bridge)
Multiplexing
  Typically share a single ADC among multiple inputs
  Need to select an input, allow time to settle before sampling
Signal Conditioning
  Amplify and filter input signal
  Protect against out-of-range inputs with clamping diodes

## Slide 18: Sample and Hold Devices
Some A/D converters require the input analog signal to be held constant during conversion (e.g. successive approximation devices)
In other cases, peak capture or sampling at a specific point in time requires a sampling device.
A “sample and hold” circuit performs this operation
Many A/D converters include a sample and hold circuit

## Slide 19: KL25 Analog Interfacing Peripherals

## Slide 20: Sources of Information
KL25 Subfamily Reference Manual (Rev. 1, June 2012)
  Describes architecture of peripherals and their control registers
  Digital to Analog Converter
    Chapter 30 of KL25 Subfamily Reference Manual
  Analog Comparator
    Chapter 29 of KL25 Subfamily Reference Manual
  Analog to Digital Converter
    Chapter 28 of KL25 Subfamily Reference Manual
KL25 Sub-family Data Sheet (Rev. 3, 9/19/2012)
  Describes circuit-specific performance parameters: operating voltages, min/max speeds, cycle times, delays, power and energy use

## Slide 21: KL25Z Analog Interface Pins
80-pin QFP
Inputs
  1 16-bit ADC with 14 input channels
  1 comparator with 6 external inputs, one 6-bit DAC
Output
  1 12-bit DAC
Notes: The MCU has multiple analog inputs and one analog output

## Slide 22: Freedom KL25Z Analog I/O
Inputs
  14 external ADC channels
  6 external comparator channels
Output
  1 12-bit DAC

## Slide 23: Using a Pin for Analog Input or Output
Configuration
  Direction
  MUX
Data
  Output (different ways to access it)
  Input
Notes: In order to use a pin for as an analog input or output we need to configure the pin control multiplexer to connect to the correct peripheral rather than the GPIO port circuitry.

## Slide 24: Pin Control Register to Select MUX Channel
MUX field of PCR defines connections
MUX (bits 10-8) | Configuration
000 | Digital circuits disabled, analog enabled
001 | Alternative 1 – GPIO
010 | Alternative 2
011 | Alternative 3
100 | Alternative 4
101 | Alternative 5
110 | Alternative 6
111 | Alternative 7
PORTC->PCR[7] &= ~PORT_PCR_MUX_MASK;
PORTC->PCR[7] |= PORT_PCR_MUX(0);
Notes: Here we see the pin control register for pins PTC7 and PTC8. We need to set the mux bits to 000 to select the analog functionality (Comparator 0 inputs 1 and 2).

## Slide 25: Digital to Analog Converter

## Slide 26: DAC Overview
Load DACDAT with 12-bit data N
MUX selects a node from resistor divider network to create Vo = (N+1)*Vin/212
Vo is buffered by output amplifier to create Vout
  Vo =Vout but Vo is high impedance - can’t drive much of a load, so need to buffer it
Notes: The Digital to Analog Converter (DAC) generates an output voltage by scaling its input reference voltage by a fraction between 0 and 1, equal to (N+1)/212.

## Slide 27: DAC Operating Modes
Normal
  DAT0 is converted to voltage immediately
Buffered
  Data to output is stored in 16-word buffer
  Next data item is sent to DAC when a selectable trigger event occurs
    Software Trigger - write to DACSWTRG field in DACx_C0
    Hardware Trigger - from PIT timer peripheral
  Normal Mode
    Circular buffer
  One-time Scan Mode
    Pointer advances until reaching upper limit of buffer, then stops
  Status flags in DACx_SR

## Slide 28: DAC Control Register 0: DACx_C0
DACEN - DAC Enabled when 1
DACRFS - DAC reference voltage select
  0: DACREF_1. Connected to VREFH
  1: DACREF_2. Connected to VDDA
LPEN - low-power mode
  0: High-speed mode. Fast (15 us settling time) but uses more power (up to 900 uA supply current)
  1: Low-power mode. Slow (100 us settling time) but more power-efficient (up to 250 uA supply current)
Additional control registers used for buffered mode

## Slide 29: DAC Control Register 1: DACx_C1
DACBFEN
  0: Disable buffer mode
  1: Enable buffer mode
DACBFMD - Buffer mode select
  0: Normal mode (circular buffer)
  1: One-time scan mode

## Slide 30: DAC Data Registers
These registers are only eight bits long
DATA[11:0] stored in two registers
  DATA0: Low byte [7:0] in DACx_DATnL
  DATA1: High nibble [11:0] in DACx_DATnH

## Slide 31: Example: Waveform Generator
Supply clock to DAC0 module
  Bit 31 of SIM SCGC6
Set Pin Mux to Analog (0)
Enable DAC
Configure DAC
  Reference voltage
  Low power mode?
  Normal mode (not buffered)
Write to DAC data register

## Slide 32: Analog Comparator

## Slide 33: Example: Power Failure Detection
Need warning of when power has failed
  Very limited amount of time before capacitor C2 discharges
  Save critical information
  Turn off output devices
  Put system into safe mode
Can use a comparator to compare Vin against a fixed reference voltage VRef

## Slide 34: Comparator Overview
Comparator compares INP and INM
CMPO Output indicates if INP>INM (1) or INP<INM (0)
Can generate an interrupt request (+, -, or +- edges)
ANMUX selection of one of multiple reference inputs, using PSEL and MSEL fields

## Slide 35: CMP Control Register 1 CMPx_CR1
EN: Module enable (1)
OPE: Output Pin Enable
  1: connects comparator output signal CMPO to output pin
PMODE: Power Mode Select
  0: Low speed
  1: High speed

## Slide 36: MUX Control Register CMPx_MUXCR
PSTM: Enable Pass Through Mode
PSEL: Plus Input Mux Control
  Selects which input (IN0-7) goes to the comparator’s + input
MSEL: Minus Input Mux Control
  Selects which input (IN0-7) goes to the comparator’s - input

## Slide 37: Comparator Output Processing
Notes: The output of the comparator is processed in several stages before possibly generating an interrupt or an output signal. We examine these on the next slide.

## Slide 38: Comparator Interrupt
CMPx_SCR: Status and control register
  COUT: output of comparator
  CFR: Comparator flag rising. Rising edge detected on comparator output COUT. Clear flag by writing with a 1.
  CFF: Comparator flag falling. Falling edge detected on comparator output COUT. Clear flag by writing with a 1.
  IER: 1 enables interrupt when CFR is set.
  IEF: 1 enables interrupt when CFF is set.
Can generate interrupt on matching edge
  CMSIS-defined ISR name for Comparator Interrupt is CMP0_IRQHandler
Notes: We can configure the comparator to generate an interrupt when the comparator output rises or falls, or both.

## Slide 39: Programmable Threshold for Comparator
Comparator has 6-bit DAC
Can use DAC to set threshold voltage for comparator
Supports 64 different threshold voltages

## Slide 40: DAC Control Register CMPx_DACCR
DACEN: Enable CMP DAC (1)
VRSEL: DAC reference voltage select
  0: Connected to VREFH
  1: Connected to VDD
VOSEL: Output voltage select
  VDACO = (VOSEL+1)*(Vin/64)
  VOSEL = 64*(VDACO /Vin) - 1

## Slide 41: Analog to Digital Converter

## Slide 42: ADC Overview
Uses successive approximation for conversion
Supports multiple resolutions: 16, 13, 12, 11, 10, 9, and 8 bits
Supports single-ended and differential conversions
Signed or unsigned results available
Up to 24 analog inputs supported (single-ended), 4 pairs of differential inputs
Automatic compare and interrupt for level and range comparisons
Hardware data averaging
Temperature sensor

## Slide 43: ADC System Overview
Notes: The ADC is many features and may look overwhelming initially. On the next page we will start looking at its major parts.

## Slide 44: ADC System Fundamentals
Analog Inputs
Analog Inputs
Conversion Clock
Result
Registers
A/D Converter
Notes: The heart of the ADC is the SAR converter in the center. This is driven by a conversion clock with a configurable speed to let us trade off speed, accuracy and power. The ADC will convert an analog input (or the difference between two, in differential mode) into a digital value which is placed in a result register.

## Slide 45: Using the ADC
ADC initialization
  Configure clock
  Select voltage reference
  Select trigger source
  Select input channel
  Select other parameters
Trigger conversion
Read results
Notes: Here are the basic steps to using the ADC.

## Slide 46: Clock Configuration
Select clock source with ADICLK
  Bus Clock (default)
  ADACK: Local clock, allows ADC operation while rest of CPU is in stop mode
  ALTCLK: alternate clock (MCU-specific)
Divide down selected clock by factor of ADIV, creating ADCK
Resulting ADCK must be within valid range to ensure accuracy (See KL25 Subfamily datasheet)
  1 to 18 MHz (<= 13-bit mode)
  2 to 12 MHz (16-bit mode)

## Slide 47: Clock Configuration Registers
ADCx_CFG1
  ADIV: divide clock by 2ADIV
    00: 1
    01: 2
    10: 4
    11: 8
  ADICLK: Input clock select
    00: Bus clock
    01: Bus clock/2
    10: ALTCLK
    11: ADACK
ADCx_CFG2
  ADACKEN: Enable asynchronous clock

## Slide 48: Voltage Reference Selection
Two voltage reference pairs available
  VREFH, VREFL
  VALTH, VALTL
Select with SC2 register’s REFSEL bits
  00: VREFH, VREFL
  01: VALTH, VALTL
  10, 11: Reserved
KL25Z
  VALTH connected to VDDA
Notes: We need to select which reference voltages to use. The lower reference indicates the voltage resulting in a 0000…000 conversion, while the upper reference is for a 1111….1111 conversion result.

## Slide 49: Conversion Trigger Selection
ADTRG in SC2
  0: software trigger
  1: hardware trigger
Software trigger:
  Write to SC1A
Ping-pong buffering
  SC1A vs. SC1n
Hardware trigger:
  Rising edge of ADHWT signal
  ADHWT sources: TPM, LPTMR, PIT, RTC, EXTRG_IN, HSCMP0
Notes: We can select how to trigger the ADC. Both software and hardware triggering are available.

## Slide 50: Hardware Trigger Sources
System Integration Module
  SIM_SOPT7 register
    See section 12.2.6 of Reference Manual
ADC0ALTTRGEN: Alternate trigger enable
ADC0PRETRGSEL: ADC pre-trigger select

## Slide 51: Input Channel Selection
Two modes, selected by SC1n[DIFF] bit
  0: Single-ended
  1: Differential
Input channel selected by value of ADCH
Extras
  Reference voltages
  Temperature
  Band Gap
Notes: We can select whether the conversion is of a single channel or the difference between two channels. We also can measure other analog voltages, described on the next page.

## Slide 52: ADC Inputs on Freedom Board
ADC Channel (Single-Ended) | MCU Signal (with ALT0 multiplexer setting) | Freedom KL25Z Connector and Pin Number
0 | PTE20 | J10 1
3 | PTE22 | J10 5
4 | PTE21 (a), PTB29 (b) | J10 3 (a), J10 9 (b)
5 | PTD1 (b) | J2 12 (b)
6 | PTD5 (b) | J2 4 (b)
7 | PTE23 (a), PTD6 (b) | J10 7 (a), J2 17(b)
8 | PTB0 | J10 2
9 | PTB1 | J10 4
11 | PTC2 | J10 10
12 | PTB2 | J10 6
13 | PTB3 | J10 8
14 | PTC0 | J1 3
15 | PTC1 | J10 12
23 | PTE30 | J10 11

## Slide 53: Special Input Channels
26: Temperature Sensor
  T = 25°C - ((VTemp - VTemp25)/m)
  m = 1.715 mV/°C
  VTEMP25 = 719 mV
  VTemp is derived from ADC conversion result
27: Band Gap
  Nominally 1.0 V, +/- 3%
  Used to allow calculation of reference voltage if it is not calibrated/regulated
  Enable BG buffer by setting BGBE bit in Power Management Control REGSC
  “My ADC tells me that channel 27 returns a code of 36000, and channel 0 returns a code of 25145. So V0 = 36000/25145 * 1.0 V = 1.432 V
29, 30: Reference voltages
  29: VREFSH
  30: VREFSL

## Slide 54: Conversion Options Selection
Low power
  Set ADLPC (in ADCx_CFG1) to 1
  Slower max clock speed
Long sample time select
  Set ADLSMP (in ADCx_CFG1) to 1
  Can select longer sample time with ADLSTS bits (in ADCx_CFG2) to add 20, 16, 10 or 6 ADCK cycles)
Conversion mode
  MODE (in ADCx_CFG1)
  Sets result precision (8 through 16 bits)
Continuous vs. single conversion
  Set ADCO (in ADCx_SC3) to 1 for continuous conversions

## Slide 55: Conversion Completion
Signaled by COCO bit in SC1n
Can generate conversion complete interrupt if AIEN in SC1 is set
  CMSIS-defined ISR name for ADC Interrupt is ADC0_IRQHandler

## Slide 56: Result Registers
Optional output processing before storage in result registers
  Offset subtraction from calibration
  Averaging: 1, 4, 8, 16 or 32 samples
  Formatting: Right justification, sign- or zero-extension to 16 bits
  Output comparison
Two result registers RA and Rn
  Conversion result goes into register corresponding to SC1 register used to start conversion (SC1A, SC1n)

## Slide 57: Output Averaging
Accumulate and average multiple samples before writing the averaged result to the result register
Result rate = sample rate / averaging factor
SC3 register
  AVGE: average enable
  AVGS: average sample count
AVGE | AVGS | Number of samples averaged
0 | xx | 1
1 | 00 | 4
1 | 01 | 8
1 | 10 | 16
1 | 11 | 32

## Slide 58: Automatic Compare
Can ignore ADC result based on comparison with CV1 and CV2
  Above or equal to threshold
  Below threshold
  Outside range
  Inside range
Ignored result…
  Not saved to RA/Rn
  CoCo not set

## Slide 59: Conversion Time Requirements
Conversion time depends on multiple factors
  Precision in bits
  Single-ended vs. differential
  Adders: LST, HSC, SFC
  Averaging
Precision (bits) | Mode | Base Conversion Time BCT
8 | single-ended | 17 ADCK cycles
9 | differential | 27
10 | single-ended | 20
11 | differential | 30
12 | single-ended | 20
13 | differential | 30
16 | single-ended | 25
16 | differential | 34

## Slide 60: Using ADC Values
The ADC gives an integer representing the input voltage relative to the reference voltages
Several conversions may be needed
  For many applications you will need to compute the approximate input voltage
    Vin = …
  For some sensor-based applications you will need to compute the physical parameter value based on that voltage (e.g. pressure) – this depends on the sensor’s transfer function
  You will likely need to do additional computations based on this physical parameter (e.g. compute depth based on pressure)
Data type
  It’s likely that doing these conversions with integer math will lead to excessive loss of precision, so use floating point math
  AFTER you have the application working, you can think about accelerating the program using fixed-point math (scaled integers).
Sometimes you will want to output ASCII characters (to the LCD, for example). You will need to convert the floating point number to ASCII using sprintf, ftoa, or another method.