## Slide 1: Timer Peripherals

## Slide 2: KL25 Timer Peripherals
PIT - Periodic Interrupt Timer
  Can generate periodically generate interrupts or trigger DMA (direct memory access) transfers
TPM - Timer/PWM Module
  Connected to I/O pins, has input capture and output compare support
  Can generate PWM signals
  Can generate interrupts and DMA requests
LPTMR - Low-Power Timer
  Can operate as timer or counter in all power modes (including low-leakage modes)
  Can wake up system with interrupt
  Can trigger hardware
Real-Time Clock
  Powered by external 32.768 kHz crystal
  Tracks elapsed time (seconds) in 32-bit register
  Can set alarm
  Can generate 1Hz output signal and/or interrupt
  Can wake up system with interrupt
SYSTICK
  Part of CPU core’s peripherals
  Can generate periodic interrupt

## Slide 3: Timer/Counter Peripheral Introduction
Common peripheral for microcontrollers
Based on presettable binary counter, enhanced with configurability
Two basic modes
  Counter mode: count pulses which indicate events (e.g. odometer pulses)
  Timer mode: clock source is periodic, so counter value is proportional to elapsed time (e.g. stopwatch)
Main configurable options
  Current count value
  Count reload value
  Count direction: up or down
  Counter’s clock source
  Counter’s overflow/underflow action
    Generate interrupt
    Reload counter, resume counting
    Toggle hardware output signal
    Stop!
Events
Clock
Current Count
Reload Value
Presettable Binary Counter
÷2 or RS
PWM
Interrupt
Reload
or

## Slide 4: Periodic Interrupt Timer

## Slide 5: Periodic Interrupt Timer
Generates periodic interrupts using a 32-bit counter
Load start value (32-bit) from LDVAL
Counter decrements with each clock pulse
  Fixed clock source for PIT - Bus Clock from Multipurpose Clock Generator - e.g. 24 MHz
When timer value (CVAL) reaches zero
  Generates interrupt
  Reloads timer with start value
Clock
Read current timer value (TVL) from PIT_CVALn
Presettable Binary Counter
Interrupt
Reload
Start Value
Read/write timer start value (TSV) from PIT_LDVALn

## Slide 6: Periodic Interrupt Timer
Write 1000 to TSV
Enabling timer loads counter with 1000, starts counting
TVL counts down to 0
PIT interrupt generated, counter reloads with 1000, starts counting
Write 700 to TSV
PIT interrupt generated, counter reloads with 400, starts counting
PIT interrupt generated, counter reloads with 400, starts counting
PIT interrupt generated, counter reloads with 400, starts counting
PIT Interrupt

## Slide 7: PIT Configuration
1: Enable clock gating!
  SIMCGC6 PIT
2: Module Control Register (PIT->MCR)
  MDIS - Module disable
    0: module enabled
    1: module disabled (clock disabled)
  FRZ - Freeze - stops timers in debug mode
    0: timers run in debug mode
    1: timers are frozen (don’t run) in debug mode
Multiple channels within a PIT
  KL25Z has two channels
Can chain timers together to create 64-bit timer

## Slide 8: Control of Each Timer Channel n
CMSIS Interface:
  General PIT settings accessed as struct: PIT->MCR, etc.
  Channels are accessed as an array of structs: PIT->CHANNEL[n].LDVAL, etc
PIT_LDVALn: Load value (PIT->CHANNEL[n].LDVAL)
PIT_CVALn: Current value (PIT->CHANNEL[n].CVAL)
PIT_TCTRLn: Timer control (PIT->CHANNEL[n].TCTRL)
  CHN: Chain
    0: independent timer operation, uses own clock source
    1: timer n is clocked by underflow of timer n-1
  TIE: Timer interrupt enable
    0: Timer will not generate interrupts
    1: Interrupt will be requested on underflow (i.e. when TIF is set)
  TEN: Timer enable
    0: Timer will not count
    1: Timer is enabled, will count
PIT_TFLGn: Timer flags
  TIF: Timer interrupt flag
    1: Timeout has occurred

## Slide 9: Configuring the PIT
Enable clock to PIT module
  SIM->SCGC6 |= SIM_SCGC6_PIT_MASK;
Enable module, freeze timers in debug mode
  PIT->MCR &= ~PIT_MCR_MDIS_MASK;
  PIT->MCR |= PIT_MCR_FRZ_MASK;
Initialize PIT0 to count down from starting_value
  PIT->CHANNEL[0].LDVAL = PIT_LDVAL_TSV(starting_value);
No chaining of timers
  PIT->CHANNEL[0].TCTRL &= ~PIT_TCTRL_CHN_MASK;

## Slide 10: Calculating Load Value
Goal: generate an interrupt every T seconds
LDV = round(T*fcount - 1)
  -1 since the counter counts down to 0
  Round since LDV register is an integer, not a real number
    Rounding provides closest integer to desired value, resulting in minimum timing error
Example: Interrupt every 137.41 ms
  LDV = 137.41 ms * 24 MHz - 1 = 3297839
Example: Interrupt with a frequency of 91 Hz
  LDV = (1/91 Hz)*24 MHz - 1 = round (263735.2637-1) = 263734

## Slide 11: Configuring the PIT and NVIC for Interrupts
Configure PIT
  Let the PIT channel generate interrupt requests
    PIT->CHANNEL[0].TCTRL |= PIT_TCTRL_TIE_MASK;
Configure NVIC
  Set PIT IRQ priority
    NVIC_SetPriority(PIT_IRQn, 128); // 0, 64, 128 or 192
  Clear any pending IRQ from PIT
    NVIC_ClearPendingIRQ(PIT_IRQn);
  Enable the PIT interrupt in the NVIC
    NVIC_EnableIRQ(PIT_IRQn);
Make sure interrupts are not masked globally
    __enable_irq();

## Slide 12: Interrupt Handler
One interrupt for entire PIT
CMSIS ISR name: PIT_IRQHandler
ISR activities
  Determine which channel triggered interrupt
    if (PIT->CHANNEL[n].TFLG & PIT_TFLG_TIF_MASK) {
  Clear interrupt request flag for channel by writing one to it
    PIT->CHANNEL[0].TFLG |= PIT_TFLG_TIF_MASK;
  Do the ISR’s work

## Slide 13: Starting and Stopping the Timer Channel
Start the timer channel
  PIT->CHANNEL[0].TCTRL |= PIT_TCTRL_TEN_MASK;
Stop the timer channel
  PIT->CHANNEL[0].TCTRL &= ~PIT_TCTRL_TEN_MASK;

## Slide 14: Example: Stopwatch
Measure time with 100 us resolution
Display elapsed time, updating screen every 10 ms
Controls
  S1: toggle start/stop
Use PIT
  Counter increment every 100 us
    Set to PIT Channel 0 to expire every 100 us
    Calculate load value LDVAL = round (100 us * 24 MHz -1) = 2399
  LCD Update every 10 ms
    Update LCD every nth PIT ISR
    n = 10 ms/100us = 100
    Don’t update LCD in ISR! Too slow.
    Instead set flag LCD_Update in ISR, poll it in main loop

## Slide 15: Timer/PWM Module (TPM)

## Slide 16: TPM - Timer/PWM Module
Core: Module counter
  Two clock options - external or internal
  Prescaler to divide clock by 1 to 128
  16-bit counter
    Can count up or up/down
    Can reload with set load value or wrap around (to FFFF or 0000)
Multiple (6) independent channels
  3 modes
    Capture Mode: capture timer’s value when input signal changes
    Output Compare: Change output signal when timer reaches certain value
    PWM: Generate pulse-width-modulated signal. Width of pulse is proportional to specified value.
  Each channel can generate interrupt, DMA request, hardware trigger on overflow
  One I/O pin per channel: TPM_CHn

## Slide 17: Timer Configuration
Clock source
  CMOD: selects internal or external clock
Prescaler
  PS: divide selected clock by 1, 2, 4, 8, 16, 32,64, 128
Count Mode: direction
  CPWMS: count up (0) or up & down (1)
Count Modulus: value to counts up to
  MOD: 16-bit
  Timer overflows when counter goes past MOD value
  Up counting: 0, 1, 2, … MOD, 0/Overflow, 1, 2, … MOD
  Up/down counting: 0, 1, 2, … MOD, MOD-1/Interrupt, MOD-2, … 2, 1, 0, 1, 2, …
DMA: Enable DMA transfer on overflow
TOF: Flag indicating timer has overflowed

## Slide 18: Basic Counter Mode
Count external events applied on input pin
  Set CMOD = 01 to select external clock
  Set PS = 000 (unless division needed
Timer overflow flag TOF set to 1 upon receiving MOD * prescaler pulses
Can generate interrupt if TOIE is set
2-0 PS | Prescaler Factor
000 | 1
001 | 2
010 | 4
011 | 8
100 | 16
101 | 32
110 | 64
111 | 128

## Slide 19: Count Mode and Modulo - Counting Up
Counter increments with each clock tick
When counter reaches MOD,
  set TOF bit (timer overflow)
  reset counter value to 0
Frequency of overflows is timer clock frequency / (1 + MOD)

## Slide 20: Count Mode and Modulo - Counting Up and Down
Up-counting phase
  Counter increments with each clock tick
  When counter reaches MOD, set TOF bit (timer overflow), set to down-count mode
Down-counting phase
  Counter decrements with each clock tick
  When counter reaches 0, set to up-count mode
Frequency of overflows is timer clock frequency / (2 * MOD)

## Slide 21: TPM Configuration (TPMx_CONF)
TRGSEL - input trigger select
CROT - counter reload on trigger
CSOO - counter stop on overflow
CSOT - counter start on trigger
GTBEEN - external global time base enable (rather than LPTPM counter)
DBGMODE - let LPTPM counter increment during debug mode
DOZEEN - pause LPTPM when in doze mode

## Slide 22: TPM Status (TPMx_STATUS)
TOF - Counter has overflowed
CHxF - Channel event has occurred (event depends on mode)

## Slide 23: Major Channel Modes
Input Capture Mode
  Capture timer’s value when input signal changes
    Rising edge, falling edge, both
  How long after I started the timer did the input change?
    Measure time delay
Output Compare Mode
  Modify output signal when timer reaches specified value
    Set, clear, pulse, toggle (invert)
  Make a pulse of specified width
  Make a pulse after specified delay
Pulse Width Modulation
  Make a series of pulses of specified width and frequency

## Slide 24: Channel Configuration and Value
Configuration: TPMx_CnSC
  CHF - set when event occurs
  CHIE - enable channel to generate an interrupt
  MSB:MSA - mode select
  ELSB:ELSA - edge or level select
  DMA - enable DMA transfers
Value: TPMx_CnV
  16-bit value for output compare or input capture

## Slide 25: Input Capture Mode
Select mode with CPWMS = 0, MSnB:MSnA = 00
TPM_CHn I/O pin operates as edge- sensitive input
  ELSnB:ELSnA select rising (01) or falling edge (10) or both (11)
When valid edge is detected on TPM_CHn…
  Current value of counter is stored in CnV
  Interrupt is enabled (if CHnIE = 1)
  CHnF flag is set (after 3 clock delay)
TPM_CHn
CnV
initialized value
3

## Slide 26: Wind Speed Indicator (Anemometer)
Rotational speed (and pulse frequency) is proportional to wind velocity
Two measurement options:
  Frequency (best for high speeds)
  Width (best for low speeds)
Can solve for wind velocity v
How can we use the TPM for this?
  Use Input Capture Mode to measure period of input signal

## Slide 27: TPM Capture Mode for Anemometer
Configuration
  Set up TPM to count at given speed from internal clock
  Set up TPM channel for input capture on rising edge
Operation: Repeat
  First TPM interrupt - on rising edge
    Reconfigure channel for input capture on falling edge
    Clear TPM counter, start it counting
  Second TPM interrupt - on falling edge
    Read capture value from CnV, save for later use in wind speed calculation
    Reconfigure channel for input capture on rising edge
    Clear TPM counter, start it counting

## Slide 28: Output Compare Mode
Select mode with CPWMS = 0, MSnA = 1
TPM_CHn I/O pin operates as output
When CNT matches CnV …
  Output signal TPM_CHn is updated
  CHnF flag is set
  CHnI Interrupt is enabled (if CHnIE = 1)
Can select one of multiple output signal actions on match
  Toggle, clear, set, pulse low, pulse high
MSnB | ELSnB | ELSnA | Output Action
0 | 0 | 1 | Toggle
0 | 0 | 0 | Clear
0 | 1 | 1 | Set
1 | 1 | 0 | Pulse low
1 | x | 1 | Pulse high
Events
CNT | 3 | 0 | 1 | 2 | 3 | 4 |  | 0 | 1 | 2 | 3
CnV | 2 | 2 | 2 | 2 | 2 | 2 |  | 2 | 2 | 2 | 2
TPM_CHn |  |  |  |  |  |  |  |  |  |  | 
CHnF | 0 | 0 | 0 | 1 | 1 | 1 |  | 1 | 1 | 1 | 1

## Slide 29: Pulse-Width Modulation
Allows a single digital signal to send more than two values (0, 1)
Simple encoding: value is the fraction of time signal is a 1
Signal can easily be averaged to create an analog voltage
PWM signal characteristics
  Modulation frequency – how many pulses occur per second (fixed)
  Period – 1/(modulation frequency)
  On-time – amount of time that each pulse is on (asserted)
  Duty-cycle – on-time/period
  Adjust on-time (hence duty cycle) to represent the analog value

## Slide 30: Uses of Pulse-Width Modulation
Digital communication is less sensitive to noise than analog methods
  PWM provides a digital encoding of an analog value
  Much less vulnerable to noise
Digital power amplifiers are more efficient and less expensive than analog power amplifiers
  Applications: motor speed control, light dimmer, switch-mode power conversion
  Load (motor, light, etc.) responds slowly, averages PWM signal

## Slide 31: Edge-Aligned PWM Mode
Edge-aligned - leading edges of signals from all PWM channels are aligned
  Uses count up mode
  Period = (MOD + 1) cycles
  Pulse width = (CnV) cycles
MSnB:MSnA = 01, CPWMS = 0
  ELSnB:ELSnA = 10 - high-true pulses
  ELSnB:ELSnA = x1 - low-true pulses

## Slide 32: Center-Aligned PWM Mode
Center-aligned - centers of signals from all PWM channels are aligned
  Uses count up/down mode
  Period = 2*MOD cycles. 0x0001 <= MOD <= 0x7FFFF
  Pulse width = 2*CnV cycles
MSnB:MSnA = 10, CPWMS = 1
  ELSnB:ELSnA = 10 - high-true pulses
  ELSnB:ELSnA = x1 - low-true pulses

## Slide 33: Servo Motor
Components
  Motor
  Gearbox
  Output shaft with crown and position sensor
  Control system
Inputs
  Power & Ground
  PWM control signal
Control system
  Moves motor to commanded position
  Uses position sensor for feedback
Gearing from motor to output shaft
  Increases torque, reduces speed
Limited range of rotation (e.g. 90⁰), can’t do full rotation
Controller
Motor
Gearbox
Pos. Sensor
Arms/Crown
Commanded Position
Actual Position

## Slide 34: Using PWM to Drive a Servo Motor
PWM signal tells servo desired shaft angle
  20 ms period (50 Hz frequency)
  1 to 2 ms pulse width
Position proportional to pulse width
  1.5 ms: centered (neutral)
  <1.5 ms: counter-clockwise
  >1.5 ms: clockwise

## Slide 35: Low Power Timer (LPTMR)

## Slide 36: LPTMR Overview
16 bit up-counter which operates in all power modes (stop, wait, etc.)
Can count time or external pulses
Glitch filter removes high-frequency noise from pulses
Can generate interrupt when counter matches compare value
Interrupt wakes MCU from any low power mode
Registers
  Counter register LPTMRx_CNR
  Compare register LPTRMx_CMR
  Prescale register LPTMRx_PSR
  Control Status register LPTMRx_CSR
Prescaler/ Glitch Filter
16-bit Counter CNR
Compare Value CMR
Comparator
LPTMR Interrupt and Hardware Trigger

## Slide 37: Prescale Register
PRESCALE: divide by 2 to 65536
  Time counter mode: Divide input clock by 2PRESCALE+1
  Pulse counter mode: Is glitch filter which recognizes input signal change after 2PRESCALE rising clock cycles
PBYP: Prescaler Bypass
  0: use prescaler
  1: bypass prescaler
PCS: Prescaler Count Select
  Inputs available depend on chip configuration, see KL25 SRM Chapter 3: Chip Configuration
PCS | Clock Source
00 | MCGIRCLK — internal reference clock (not available in LLS and VLLS modes)
01 | LPO — 1 kHz clock (not available in VLLS0 mode)
10 | ERCLK32K (not available in VLLS0 mode when using 32 kHz oscillator)
11 | OSCERCLK — external reference clock (not available in VLLS0 mode)

## Slide 38: Control Status Register
TCF: Timer Compare Flag
  1 if CNR matches CMR and increments
TIE: Timer Interrupt Enable
  Set to 1 to enable interrupt when TCF == 1
TPS: Timer Pin Select for pulse counter mode
  Inputs available depend on chip configuration, see KL25 SRM Chapter 3: Chip Configuration

## Slide 39: Control Status Register
TPP: Timer Pin Polarity
  0: input is active high, increments CNR on rising edge
  1: input is active low, increments CNR on falling edge
TFC: Timer Free-running Counter
  0: Reset CNR whenever TCF is set (on match)
  1: Reset CNR on overflow (wrap around)
TMS: Timer Mode Select
  0: Time counter
  1: Pulse counter
TEN: Timer Enable
  1: Enable LPTMR operation

## Slide 40: Watchdog Timer

## Slide 41: Watch Dog Timer (WDT) Concepts
Goal: detect if program is not refreshing WDT correctly (≈ malfunctioning?)
Mechanism:
  Program periodically tells WDT that it is OK (services the WDT)
  If timer ever overflows (times out), then program didn’t say it was OK soon enough, so reset the MCU
Typically used as a “last resort” mechanism for forcing system software back into known state
Time
WDT Value
Start WDT
WDT overflows, resets system
Service WDT
Overflow
Program State
OK
Hit a bug and hung
Reset ISR
OK

## Slide 42: Windowed Watch Dog Timer Concepts
Closed
Can only service WDT when WDT counter value is in a certain range
  Any service attempt outside the window will cause the WDT to reset the system
Windowed WDT improves reliability
  Almost eliminates likelihood of program crash which still services the WDT
Time
WDT Value
Start WDT
Service WDT in window
Overflow
Program State
OK
Hit bug
Service WDT
before window,
causing reset
Window
Window State
Closed
Open
Open
Reset ISR

## Slide 43: Kinetis KL25Z WDT (COP)
WDT is called COP (Computer Operating Properly) by Freescale
  Details in KL25 Subfamily Reference Manual, Chapter 3 (Chip Configuration)
Registers
  COPCTRL: COP Control Register (COPC in CMSIS)
  SRVCOP: Service COP register
Initializing the COP
  Write to COPCTRL
    Write-protected: Only first write to COPCTRL after a reset is recognized, subsequent writes are ignored
  Can disable COP by clearing COPCTRL[COPT]

## Slide 44: COP Configuration
Control Bits (COPCTRL) |  | Clock Source | COP Window Opens | COP Overflow Count
COPCLKS | COPT |  |  | 
n/a | 00 | n/a | n/a | COP is disabled
0 | 01 | 1 kHz | n/a | 25 cycles, 32 ms
0 | 10 | 1 kHz | n/a | 28 cycles, 256 ms
0 | 11 | 1 kHz | n/a | 210 cycles, 1024 ms
1 | 01 | Bus | 6144 cycles | 213 cycles
1 | 10 | Bus | 49152 cycles | 216 cycles
1 | 11 | Bus | 196608 cycles | 218 cycles
Default setting
Select clock source with COPCTRL[COPCLKS]
  1 kHz or bus clock (e.g. 24 MHz)
Set time-out divider with COPCTRL[COPT]
Optional Windowed operation (when using bus clock) by setting COPCTRL[COPW]
  Program must reset COP within last 25% of time-out period

## Slide 45: WDT Service and Operation
Servicing (resetting) the COP
  Reset COP timer by writing 0x55 and then 0xAA to SRVCOP during timeout period
  Writing wrong value causes COP to reset MCU immediately
Reset actions
  MCU is reset
  WDOG bit in Reset Control Module (RCM) System Reset Status Register 0 (SRS0) is set to show watchdog caused reset

## Slide 46: Determining Cause of Reset
Reset Control Module (RCM) System Reset Status Register 0 (SRS0) bits
  POR: power-on reset
  PIN: external reset pin asserted
  WDOG: COP watchdog timer timed out
  LOL: Loss of lock in PLL (clock generation)
  LOC: Loss of clock detected by MCG clock monitor
  LVD: Low voltage detected
  WAKEUP: System was asleep in low-leakage mode when a LLWU source was activated

## Slide 47: SystemInit()
SystemInit() function in system_MKL25Z4.c disables the COP WDT by default because DISABLE_WDOG is non-zero
All subsequent writes to SIM->COPC are ignored by MCU
  Including our own initialization code!
To fix this, redefine DISABLE_WDOG to 0, so the compiler ignores lines 93-95 of the source code

## Slide 48: Demonstration Code – WDT Demo
System flashes red LED on startup
Loop:
  Read accelerometer
  Calculate board inclination
  Is board flat (within 20⁰ of horizontal)?
    Yes: Light green LED and service the watchdog
    No: Light yellow LED and do NOT service the watchdog
Holding the board tilted for more than about 1 second will cause the WDT to trigger, resetting the CPU (shown by flashing red LED)

## Slide 49: WDT Best Practices
Don’t scatter WDT service commands throughout your code
  There should just be one or a few such commands in the entire program
Choose WDT period appropriately
  Too long: System is out of control long enough to get into real trouble
  Too short: You will need to reset WDT frequently in your code, complicating development with code writing and timing analysis overhead
Frequent WDT resets? (Boot loop)
  Consider logging abnormal causes of reset for later diagnosis
  Determine how production code should respond to WDT resets (rare vs. frequent)
WDT should be difficult to accidentally disable in software

## Slide 50: Using a WDT in a Multithreaded Application
Each periodic task updates a timestamp when it starts running
Checker thread
  Checks timestamp for each thread i to verify it ran recently (enough).
  If all threads are ok, restart the WDT.
  If not, allow WDT to expire.
Does this detect every possible problem?
  No, but it catches many and is far better than not using a WDT
How to deal with non-periodic tasks?
  Application-dependent!
The checker could be integrated into the scheduler – possible programming project

## Slide 51: Debugging with the WDT
How do you debug a system with a WDT?
  Don’t want MCU to reset as soon as the code hits a breakpoint!
  Need to disable WDT somehow if it isn’t done automatically
KL25 COP behavior – handles WDT automatically
  If using bus clock
    COP doesn’t increment if MCU is in debug mode or stop mode (including VLPS and LLS)
    COP resumes counting upon exiting these modes
  If using 1 kHz clock
    COP cleared to zero as long as MCU is in debug or stop mode (including VLPS and LLS)
    COP resumes counting (from zero) upon exiting these modes
  Disabled when in VLLSx mode