## Slide 1: Serial Communications

## Slide 2: Overview
Serial communications
  Concepts
  Tools
  Software: polling, interrupts and buffering
SPI communications
  Concepts
  KL25 SPI peripheral
I2C communications
  Concepts
  KL25 I2C peripheral
UART communications
  Concepts
  KL25 I2C peripheral

## Slide 3: Why Communicate Serially?
Although native word size for CPU is 32 bits, sending all of a word’s bits simultaneously has disadvantages:
  Cost and weight: larger IC package, more wires, larger connectors
  Mechanical reliability: more wires => more connector contacts to fail
  Timing complexity: some bits may arrive later than others due to variations in capacitance and resistance across conductors
  Circuit complexity and power: may not want to have 16 different transmitters + receivers in the system
Communicating serially reduces number of signals needed
80 pins
14 mm/side
196 sq. mm
32 pins
5 mm/side
25 sq. mm
20 pins
1.94 mm/side
3.76 sq. mm
Shrinking Packages for Freescale MCUs

## Slide 4: Example System
Dedicated point-to-point connections
  Parallel data lines, read and write lines between MCU and each peripheral
Fast, allows simultaneous transfers
Requires many connections, PCB area, scales badly
  Need 4*(8+2) = 40 pins on MCU to communicate!

## Slide 5: Parallel Buses
All devices use buses to share data, read and write signals
MCU uses individual select lines to address each peripheral
MCU requires fewer pins for data, but still one per data bit
    Need 4 + (8+2) = 14 pins on MCU to communicate
MCU can communicate with only one peripheral at a time

## Slide 6: Synchronous Serial Data Transmission
Use shift registers and a clock signal to convert between serial and parallel formats
Synchronous: an explicit clock signal is along with the data signal
Transmitting Device
Receiving Device
Clock
Serial Data
Data Sampling Time at Receiver

## Slide 7: Synchronous Full-Duplex Serial Data Bus
Now can use two serial data lines - one for reading, one for writing.
  Allows simultaneous send and receive full-duplex communication
  Need 4 + 3 = 7 pins on MCU to communicate

## Slide 8: Synchronous Half-Duplex Serial Data Bus
  Share the serial data line
    Need 4 + 2 = 6 pins on MCU to communicate
  Doesn’t allow simultaneous send and receive - is half-duplex communication

## Slide 9: Asynchronous Serial Communication
Eliminate the clock line!
Transmitter and receiver must generate clock locally
Transmitter must add start bit (always same value) to indicate start of each data frame
Receiver detects leading edge of start bit, then uses it as a timing reference for sampling data line to extract each data bit N at time Tbit*(N+1.5)
Stop bit is also used to detect some timing errors
Tbit*1.5
Data
bits
Data Sampling Time at Receiver
Tbit*2.5
Tbit*3.5
Tbit*4.5
Tbit*5.5
Tbit*6.5
Tbit*7.5
Tbit*8.5
Tbit*9.5
Tbit*10.5
Time Zero

## Slide 10: Serial Communication Specifics
Data frame fields
  Start bit (one bit)
  Data (LSB first or MSB, and size – 7, 8, 9 bits)
  Optional parity bit is used to make total number of ones in data even or odd
  Stop bit (one or two bits)
All devices must use the same communications parameters
  E.g. communication speed (300 baud, 600, 1200, 2400, 9600, 14400, 19200, etc.)
Sophisticated network protocols have more information in each data frame
  Medium access control – when multiple nodes are on bus, they must arbitrate for permission to transmit
  Addressing information – for which node is this message intended?
  Larger data payload
  Stronger error detection or error correction information
  Request for immediate response (“in-frame”)
Message
Data
bits

## Slide 11: Error Detection
Can send additional information to verify data was received correctly
Need to specify which parity to expect: even, odd or none.
Parity bit is set so that total number of “1” bits in data and parity is even (for even parity) or odd (for odd parity)
  01110111 has 6 “1” bits, so parity bit will be 1 for odd parity, 0 for even parity
  01100111 has 5 “1” bits, so parity bit will be 0 for odd parity, 1 for even parity
Single parity bit detects if 1, 3, 5, 7 or 9 bits are corrupted, but doesn’t detect an even number of corrupted bits
Stronger error detection codes (e.g. Cyclic Redundancy Check) exist and use multiple bits (e.g. 8, 16), and can detect many more corruptions.
  Used for CAN, USB, Ethernet, Bluetooth, etc.

## Slide 12: Tools for Serial Communications Development
Tedious and slow to debug serial protocols with just an oscilloscope
Instead use a logic analyzer to decode bus traffic
Worth its weight in gold!
Saelae 8-Channel Logic Analyzer
  $150 (www.saelae.com)
  Plugs into PC’s USB port
  Decodes SPI, asynchronous serial, I2C, 1-Wire, CAN, etc.
Build your own: with Logic Sniffer or related open-source project

## Slide 13: Software Architecture for Handling asynchronous Communication

## Slide 14: Software Structure
Communication is asynchronous to program
  Don’t know what code the program will be executing …
    when the next item arrives
    when current outgoing item completes transmission
    when an error occurs
  Need to synchronize between program and serial communication interface somehow
Options
  Polling
    Wait until data is available
    Simple but inefficient of processor time
  Interrupt
    CPU interrupts program when data is available
    Efficient, but more complex

## Slide 15: Serial Communications and Interrupts
Want to provide multiple threads of control in the program
  Main program (and subroutines it calls)
  ISR(s)
    Transmit ISR activity – executes when serial interface is ready to send another character
    Receive ISR activity – executes when serial interface receives a character
    Error ISR(s) activity – execute if an error occurs
Need a way of buffering information between threads
  Solution: circular queue with head and tail pointers
  One for tx, one for rx
Serial Interface
ISR:Tx
ISR:Rx
get_string
send_string
Main Program or other threads

## Slide 16: Enabling and Connecting Interrupts to ISRs
ARM Cortex-M0+ provides one IRQ for all of a communication interface’s events
Within ISR (IRQ Handler), need to determine what triggered the interrupt, and then service it
void UART2_IRQHandler() {
if (transmitter ready) {
if (more data to send) {
get next byte
send it out transmitter
}
}
if (received data) {
get byte from receiver
save it
}
if (error occurred) {
handle error
}
}

## Slide 17: Code to Implement Queues
Enqueue at tail: tail_ptr points to next free entry
Dequeue from head: head_ptr points to item to remove
#define the queue size to make it easy to change
One queue per direction
  ISR unloads tx_q for transmit
  ISR loads rx_q for receive
Other threads (e.g. main) load tx_q and unload rx_q
Need to wrap pointer at end of buffer to make it circular,
  Use % (modulus, remainder) operator if queue size is not power of two
  Use & (bitwise and) if queue size is a power of two
Queue is empty if size == 0
Queue is full if size == Q_SIZE
write data to tail
read data from head
older data
newer data
Serial
Interface
ISR:Tx
ISR:Rx
get_string
send_string

## Slide 18: Defining the Queues
#define Q_SIZE (32)
typedef struct {
unsigned char Data[Q_SIZE];
unsigned int Head; // points to oldest data element
unsigned int Tail; // points to next free space
unsigned int Size; // quantity of elements in queue
} Q_T;
Q_T tx_q, rx_q;
Notes: Here is the code to define the size of the queue (Q_SIZE), the data type for the queue (Q_T) and to declare two queues (tx_q and rx_q).

## Slide 19: Initialization and Status Inquiries
void Q_Init(Q_T * q) {
unsigned int i;
for (i=0; i<Q_SIZE; i++)
q->Data[i] = 0; // to simplify our lives when debugging
q->Head = 0;
q->Tail = 0;
q->Size = 0;
}
int Q_Empty(Q_T * q) {
return q->Size == 0;
}
int Q_Full(Q_T * q) {
return q->Size == Q_SIZE;
}
Notes: Here is the code for initialization and tests for empty and full.

## Slide 20: Enqueue and Dequeue
int Q_Enqueue(Q_T * q, unsigned char d) {
// What if queue is full?
if (!Q_Full(q)) {
q->Data[q->Tail++] = d;
q->Tail %= Q_SIZE;
q->Size++;
return 1; // success
} else
return 0; // failure
}
unsigned char Q_Dequeue(Q_T * q) {
// Must check to see if queue is empty before dequeueing
unsigned char t=0;
if (!Q_Empty(q)) {
t = q->Data[q->Head];
q->Data[q->Head++] = 0; // to simplify debugging
q->Head %= Q_SIZE;
q->Size--;
}
return t;
}
Notes: Here is the code to enqueue or dequeue an item.

## Slide 21: Using the Queues
Sending data:
if (!Queue_Full(…)) {
    Queue_Enqueue(…, c)
    }
Receiving data:
if (!Queue_Empty(…)) {
    c=Queue_Dequeue(…)
    }
Notes: When trying to add or remove data from a queue, we need to check to see if there is space or data available.

## Slide 22: Software Designs – Parsing Messages

## Slide 23: Decoding Messages
Two types of messages
Actual binary data sent
  Detect start of message
  Identify message type
  Optional: Confirm integrity with CRC
  Based on this message type, copy binary data from message fields into variables
    May need to use pointers and casting to get code to translate formats correctly and safely
ASCII text characters representing data sent
  Detect start of message
  Identify message type
  Optional: Confirm integrity with CRC
  Based on this message type, translate (parse) the data from the ASCII message format into a binary format
  Copy the binary data into variables

## Slide 24: Example UART Application
Many subsystems connect with the rest of the system using asynchronous serial communications
Lassen iQ GPS receiver module from Trimble
  Two full-duplex asynch. serial connections
  Three protocols supported
  Support higher speeds through reconfiguration

## Slide 25: Example Binary Serial Data: TSIP
switch (id) {
case 0x84:
lat = *((double *) (&msg[0]));
lon = *((double *) (&msg[8]));
alt = *((double *) (&msg[16]));
clb = *((double *) (&msg[24]));
tof = *((float *) (&msg[32]));
break;
case 0x4A: …
default:
break;
}
Notes: Here is an example of a binary data format used by Trimble GPS modules. Each packet begins with a <DLE> code (0x10) and then the id of the packet type. This makes code very easy to write. For example, the C Code presented decodes a packet of type 0x84 and places its fields into several floating point variables without needing any translation or additional processing.

## Slide 26: Example ASCII Serial Data: NMEA-0183
Notes: ASCII serial data is sent in a human readable form. However, this means the code to process it must convert it back to a native binary format before using it. We will see how on the next pages.

## Slide 27: State Machine for Parsing NMEA-0183
Start
Talker + Sentence Type
Sentence Body
Checksum 1
Checksum 2
$ Append char to buf.
Any char. except *, \r or \n
Append char to buf. Inc. counter
*, \r or \n, non-text, or counter>6
buf==$SDDBT, $VWVHW, or $YXXDR
Enqueue all chars. from buf
Any char. except *
Enqueue char
*
Enqueue char
Any char.
Save as checksum1
/r or /n
Any char.
Save as checksum2
Notes: We start by designing the code to decode the sentence. We wait for a $ which indicates the start of the sentence. Then we start accepting characters and transition between states based on the delimiters. After getting these fields we can work on decoding the received text (e.g. “43.781”) into actual values (e.g. a floating point variable).

## Slide 28: Parsing
switch (parser_state) {
case TALKER_SENTENCE_TYPE:
switch (msg[i]) {
‘*’:
‘\r’:
‘\n’:
parser_state = START;
break;
default:
if (Is_Not_Character(msg[i]) || n>6) {
parser_state = START;
} else {
buf[n++] = msg[i];
}
break;
}
if ((n==6) & … ){
parser_state = SENTENCE_BODY;
}
break;
case SENTENCE_BODY:
break;

## Slide 29: KL25Z and Freedom Specifics

## Slide 30: Freedom KL25Z Serial I/O
UART
SPI
I2C
Notes: The Freedom KL25Z supports three types of serial I/O across a range of pins.

## Slide 31: KL25Z Clock Gating for Serial Comm.
Set corresponding bit(s) in SIM_SCGC4 Register
Notes: Before configuring a serial peripheral, be sure to enable its clock.

## Slide 32: SPI Communications

## Slide 33: Hardware Architecture
All chips share bus signals
  Clock SCK
  Data lines MOSI (master out, slave in) and MISO (master in, slave out)
Each peripheral has its own chip select line (CS)
  Master (MCU) asserts the CS line of only the peripheral it’s communicating with

## Slide 34: Serial Data Transmission
Use shift registers and a clock signal to convert between serial and parallel formats
Synchronous: an explicit clock signal is along with the data signal
Transmitting Device
Receiving Device
Clock
Serial Data
Data Sampling Time at Receiver

## Slide 35: SPI Signal Connection Overview
SPI Communication consists of a series of data swaps between the Master and the Slave
  As the master shifts out its transmit byte, it is also shifting in the received byte from the Slave
Notes: Here we can see that the SPI communication uses two shift registers (one in the master and one in the slave) which are connected in a ring. The master exchanges the data in these two registers by sending a series of clock pulses on the SPSCK signal.

## Slide 36: SPI Control Register 1 (SPIx_C1)
SPIE: SPI interrupt enable for receive buffer full and mode fault
SPE: SPI system enable
SPTIE: SPI interrupt enable for transmit buffer empty
MSTR: select master mode
CPOL: Clock polarity
CPHA: Clock phase
SSOE: Slave select output enable

## Slide 37: Clock and Phase Settings: CPHA = 1
Notes: Here is an example of how data communication occurs in with CPHA=1. In this case, the first clock signal edge shifts out the data, and the second clock signal edge indicates it is valid. The Slave Select (SS) line does not enable the transmission of any data until the clock is asserted.

## Slide 38: Clock and Phase Settings: CPHA = 0
Notes: Here CPHA is 0. The master and slave enable their data outputs with valid data as soon as the slave select (SS) line is asserted. The first clock edge indicates the data is valid, and the second clock edge shifts out the next bit.

## Slide 39: SPI Control Register 2 (SPIx_C2)
SPMIE: SPI interrupt enable for receive data match
SPLPIE: SPI interrupt enable for wake from low-power mode
TXDMAE: Transmit DMA enable
MODFEN: Master mode-fault function enable
BIDIROE
RDDMAE: Receive DMA enable
SPISWAI: Stop SPI in wait mode
SPC0: Single wire (bidirectional) mode

## Slide 40: SPI Baud Rate Register (SPIx_BR)
SPPR: SPI baud rate prescale divisor: divides by n+1
SPR: SPI baud rate divisor: divides by 2n+1
fSPI = fbus_clock/((SPPR+1)*2SPR+1)
Notes: This register controls how quickly the SPI bus communicates. Typically SPI peripherals can communicate at very high speeds (e.g. 1 MHz, 10 MHz or more).

## Slide 41: Normal and Bidirectional Modes
Notes: The SPI peripheral can operate in bidirectional mode, in which it reduces pin count by sharing the same signal (MOMI or SISO) to send and receive data. This only allows half-duplex communication.

## Slide 42: SPI Example: Secure Digital Card Access
SD cards have two communication modes
  Native 4-bit
  Legacy SPI 1-bit
SPI mode 0
  CPHA=0
  CPOL=0
VDD from 2.7 to 3.6 V
CS: Chip Select (active low)
Source – FatFS FAT File System Module:
  http://elm-chan.org/docs/mmc/mmc_e.html
  http://elm-chan.org/fsw/ff/00index_e.html

## Slide 43: SPI Commands for SD Card
Host sends a six-byte command packet to card
  Index, argument, CRC
Host reads bytes from card until card signals it is ready
  Card returns
    0xff while busy
    0x00 when ready without errors
    0x01-0x7f when error has occurred

## Slide 44: SD Card Transactions
Single Block Read
Multiple Block Read
Single Block Write
Multipe Block Write
Notes: Here we see several examples of SPI communications with an SD Card controller. For example, the MCU sends a command (e.g. CMD17), and then polls the SD Card repeatedly until the command response indicates the data is ready. The SD Card controller then responds with the data.

## Slide 45: I2C Communications

## Slide 46: I2C Bus Overview
“Inter-Integrated Circuit” bus
Multiple devices connected by a shared serial bus
Bus is typically controlled by master device, slaves respond when addressed
I2C bus has two signal lines
  SCL: Serial clock
  SDA: Serial data
Full details available in “The I2C-bus Specification”
Notes: Note that with I2C there is no chip select line needed to address a particular slave. Instead, each I2C transaction contains an address. Only the addressed slave responds.

## Slide 47: I2C Bus Connections
Resistors pull up lines to VDD
Open-drain transistors pull lines down to ground
Master generates SCL clock signal
  Can range up to 400 kHz, 1 MHz, or more

## Slide 48: I2C Message Format
Message-oriented data transfer with four parts
  Start condition
  Slave Address transmission
    Address
    Command (read or write)
    Acknowledgement by receiver
  Data fields
    Data byte
    Acknowledgement by receiver
  Stop condition
Message is made of
  Signals: Start, Stop, Repeated Start
  Bytes
  Acknowledgement bits

## Slide 49: Master Writing Data to Slave
Notes: Here we see the series of bytes sent when a master writes data to a slave.

## Slide 50: Master Reading Data from Slave
Notes: Reading data is similar, but the slave transmits the data bytes, while the master acknowledges them.

## Slide 51: I2C Addressing: Devices and Registers
Slave device addressing
  Each slave device has a seven-bit address
  Can support up to 27=128 different devices on same bus
  Different types of device have different default addresses
  Sometimes can select a secondary default address by tying a device pin to a different logic level
Register addressing
  I2C devices may have multiple control, status, data registers and even data memory internally – how do we get at it?
  Use the first byte of data as a register address
  Example: First seven registers of MMA8451 I2C accelerometer
0x32
0x16
0x66
0x20
Master

## Slide 52: I2C with Register Addressing
Master drives communication
  Sends start condition, address of slave, read/write command
  Listens for acknowledgement from slave
  Sends register address (byte)
  Listens for acknowledgement from slave

## Slide 53: KL25Z I2C Controller
Notes: Here is an overview of the I2C controller in the MCU. The core parts are the in/out data shift register and clock control, but other logic has been added for I2C features.

## Slide 54: Setting the I2C Baud Rate
I2Cx_F: Frequency Divider register
  MULT: specified multiplier mul = 2MULT
    valid values: 1, 2,4
  ICR: Clock Rate
  I2C baud rate = fbus/ (2MULT * ICR)
Notes: I2C baud rates are generally much slower than SPI, running at 100 kHz, 400 kHz, or maybe 1 MHz.

## Slide 55: I2C Control Register 1 – I2Cx_C1
IICEN - enable I2C module
IICIE - enable I2C interrupt
MST - select master mode
  01 generates Start condition
  10 generates Stop condition
TX – Select 1 for master transmit and 0 for master receive
TXAK – Transmit Acknowledge enable
RSTA – Repeat Start
WUEN – Wakeup enable
DMAEN – Enable DMA

## Slide 56: I2C Status Register – I2Cx_S
TCF – Transfer Complete flag set after transferring byte and acknowledge bit
IAAS – Addressed as a Slave
BUSY – bus busy
ARBL – arbitration lost
RAM – Range address match
SRW – when slave, indicates transmission direction (0: slave receive, 1: slave transmit)
IICIF: Interrupt pending flag
RXAK: 0: acknowledge signal received

## Slide 57: I2C Data Register – I2Cx_D
8-bit data register
Master transmit mode
  Writing to I2Cx_D starts a data transfer
Master receive mode
  Reading from I2Cx_D starts reception of next byte

## Slide 58: Macros for Polled Communications
#define I2C_M_START I2C0->C1 |= I2C_C1_MST_MASK
#define I2C_M_STOP I2C0->C1 &= ~I2C_C1_MST_MASK
#define I2C_M_RSTART I2C0->C1 |= I2C_C1_RSTA_MASK
#define I2C_TRAN I2C0->C1 |= I2C_C1_TX_MASK
#define I2C_REC I2C0->C1 &= ~I2C_C1_TX_MASK
#define BUSY_ACK while(I2C0->S & 0x01)
#define TRANS_COMP while(!(I2C0->S & 0x80))
#define I2C_WAIT while((I2C0->S & I2C_S_IICIF_MASK)==0){} \
I2C0->S |= I2C_S_IICIF_MASK;
#define NACK I2C0->C1 |= I2C_C1_TXAK_MASK
#define ACK I2C0->C1 &= ~I2C_C1_TXAK_MASK
Notes: The file i2c.h has useful macros for busy-wait I2C communications.

## Slide 59: Writing a Single Byte to a Device
I2C_TRAN; /*set to transmit mode */
I2C_M_START; /*send start */
I2C0->D = dev; /*send dev address */
I2C_WAIT; /*wait for ack */
I2C0->D = address; /*send write address */
I2C_WAIT;
I2C0->D = data; /*send data */
I2C_WAIT;
I2C_M_STOP;

## Slide 60: Reading a Single Byte from a Device
I2C_TRAN; /*set to transmit mode */
I2C_M_START; /*send start */
I2C0->D = dev; /*send dev address */
I2C_WAIT; /*wait for completion */
I2C0->D = address; /*send read address */
I2C_WAIT; /*wait for completion */
I2C_M_RSTART; /*repeated start */
I2C0->D = (dev|0x1); /*send dev address (read) */
I2C_WAIT; /*wait for completion */
I2C_REC; /*set to recieve mode */
NACK; /*set NACK after read */
data = I2C0->D; /*dummy read */
I2C_WAIT; /*wait for completion */
I2C_M_STOP; /*send stop */
data = I2C0->D; /*read data */

## Slide 61: Reading Multiple Bytes from a Device: Set Up
I2C_TRAN; /*set to transmit mode */
I2C_M_START; /*send start */
I2C0->D = dev; /*send dev address */
I2C_WAIT; /*wait for ack */
I2C0->D = address; /*send read address */
I2C_WAIT; /*wait for completion */
I2C_M_RSTART; /*repeated start */
I2C0->D = (dev|0x1); /*send dev address (read) */
I2C_WAIT; /*wait for completion */
I2C_REC; /*set to receive mode */

## Slide 62: Reading Multiple Bytes from a Device: Data
// For each byte
if(isLastRead) {
NACK; /*set NACK after read */
} else {
ACK; /*ACK after read */
}
data = I2C0->D; /*dummy read */
I2C_WAIT; /*wait for completion */
if(isLastRead) {
I2C_M_STOP; /*send stop */
}
data = I2C0->D; /*read real data */
Notes: Reading multiple bytes accelerates communication by reducing the overhead of setting up multiple transactions.

## Slide 63: Interrupt-Driven I2C Communications
Example flowchart from KL25Z Reference Manual chapter on I2C peripheral
One ISR handles all possible cases
  Is MCU is in master or slave mode?
  Arbitration lost (in multi-master bus)?
  Transmit or receive?
  More data to send?
  Acknowledge received?
  etc.

## Slide 64: Example I2C Peripheral: 3-Axis Accelerometer
Freescale MMA8451, included in Freedom KL25Z board
  Freedom KL26Z board has 3-axis accelerometer and 3-axis magnetometer (compass)
Can measure acceleration in x/y/z directions up to ±2g, ± 4g, ± 8g
Can compute rotation about x/y axes (pitch, roll)
I2C addresses are 0x3A (read) and 0x3B (write)
  011101r (r=1 for read, r=0 for write)

## Slide 65: MMA8451 on Freedom KL25Z
Notes: Here we see where the accelerometer is located on the Freedom board, the circuit, and the x/y/z axis orientations.

## Slide 66: Main Registers of Interest in MMA8451
Acceleration Data
  Signed (two’s complement) data
  14 or 8 bits per channel (left aligned)
  X-axis: 0x01, 0x02
  Y-axis: 0x03, 0x04
  Z-axis: 0x05, 0x06
Resolution is about 1/4096 g per LSB (in +/- 2 g mode)
Who Am I?
  Used to identify which device this is (IC-specific)
  Device ID - 0x1A

## Slide 67: Control Register 1 (0x2A)
ACTIVE: set to 1 to put in active (not standby) mode
FREAD: set to 1 to fast read just 8 MSBs of XYZ data
LNOISE: low noise mode
DR2-0: select output data rate from 1.56 Hz to 800 Hz
ASLP_RATE1-0: Select Sleep mode rate from 1.56 to 50 Hz
DR2 | DR1 | DR0 | Output Data Rate
0 | 0 | 0 | 800 Hz
0 | 0 | 1 | 400
0 | 1 | 0 | 200
0 | 1 | 1 | 100
1 | 0 | 0 | 50
1 | 0 | 1 | 12.5
1 | 1 | 0 | 6.25
1 | 1 | 1 | 1.56

## Slide 68: Registers for Additional Features
FIFO configuration
Interrupt control and status
Dynamic range
High-pass filter configuration
Portrait/Landscape detection settings
Freefall detection settings
Sleep control registers
Offset per axis
Transient event detection settings
Tap (pulse) detection settings
Notes: The device supports many additional features which can be configured with their own control registers.

## Slide 69: Demonstration: Configure the Accelerometer
Source code in mma8451.c
Basic approach
  Read byte from the WHOAMI register, verify it matches expected value for MMA8451
  Delay…
  Set to active, 14-bit mode, 100 Hz sampling rate
if(i2c_read_byte(MMA_ADDR, REG_WHOAMI) == WHOAMI) {
Delay(10);
//set active, 14 bit data and 100 Hz ODR (0x19)
i2c_write_byte(MMA_ADDR, REG_CTRL1, 0x01);
return 1;
}

## Slide 70: Demonstration: Read the Accelerations
Send I2C Start condition
Send read addresses (device and register)
Read first five bytes of data into data[i]
Read last byte of data into data[i] (also sends stop condition)
Append bytes to form 16-bit words (int16_t)
Divide by four to adjust for scaling
i2c_start();
i2c_read_setup(MMA_ADDR , REG_XHI);
for( i=0;i<5;i++) {
data[i] =
i2c_repeated_read(1);
}
data[i] = i2c_repeated_read(0);
for ( i=0; i<3; i++ ) {
temp[i] = (int16_t)
((data[2*i]<<8) |
data[2*i+1]);
}
// Right-justify, is 14 bits
acc_X = temp[0]/4;
acc_Y = temp[1]/4;
acc_Z = temp[2]/4;

## Slide 71: Asynchronous serial (UART) Communications

## Slide 72: Transmitter Basics
If no data to send, keep sending 1 (stop bit) – idle line
When there is a data word to send
  Send a 0 (start bit) to indicate the start of a word
  Send each data bit in the word (use a shift register for the transmit buffer)
  Send a 1 (stop bit) to indicate the end of the word
Tbit
Data
bits
Data Sampling Time at Receiver
Time Zero
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit

## Slide 73: Receiver Basics
Wait for a falling edge (beginning of a Start bit)
  Then wait ½ bit time
  Do the following for as many data bits in the word
    Wait 1 bit time
    Read the data bit and shift it into a receive buffer (shift register)
  Wait 1 bit time
  Read the bit
    if 1 (Stop bit), then OK
    if 0, there’s a problem!
Tbit*1.5
Data
bits
Data Sampling Time at Receiver
Tbit*2.5
Tbit*3.5
Tbit*4.5
Tbit*5.5
Tbit*6.5
Tbit*7.5
Tbit*8.5
Tbit*9.5
Tbit*10.5
Time Zero

## Slide 74: For this to work…
Transmitter and receiver must agree on several things (protocol)
  Order of data bits
  Number of data bits
  What a start bit is (1 or 0)
  What a stop bit is (1 or 0)
  How long a bit lasts
    Transmitter and receiver clocks must be reasonably close in frequency, since the only timing reference is the start of the start bit

## Slide 75: KL25 UARTs
UART: Universal (configurable) Asynchronous Receiver/Transmitter
UART0
  Low Power
  Can oversample from 4x to 32x
  Is used by debugger MCU on Freedom KL25Z, so not available
UART1, UART2
  More basic, fewer features, easier to program

## Slide 76: UART Transmitter
Notes: The heart of the transmitter is a parallel-to-serial shift register which holds the data to send, parity, a start bit (Low, 0) and a stop bit (High, 1). This information is shifted out to the TxD pin.

## Slide 77: UART Receiver
Notes: The receiver contains a serial-to-parallel shift register which accepts incoming data and verifies it is formatted correctly.

## Slide 78: Input Data Oversampling
When receiving, UART oversamples incoming data line
  Extra samples allow voting, improving noise immunity
  Better synchronization to incoming data, improving noise immunity
UART0 provides configurable oversampling from 4x to 32x
  Put desired oversampling factor minus one into UART0 Control Register 4, OSR bits.
UART1, UART2 have fixed 16x oversampling

## Slide 79: Baud Rate Generator
Need to divide module clock frequency down to desired baud rate * oversampling factor
Example
  24 MHz -> 4800 baud with 16x oversampling
  Division factor = 24E6/(4800*16) = 312.5. Must round to closest integer value ( 312 or 313), will have a slight frequency error.

## Slide 80: Using the UART
When can we transmit?
  Transmit buffer must be empty
  Can poll UARTx->S1 TDRE flag
  Or we can use an interrupt, in which case we will need to queue up data
Put data to be sent into UARTx_D (UARTx->D in with CMSIS)
When can we receive a byte?
  Receive buffer must be full
  Can poll UARTx->S1 RDRF flag
  Or we can use an interrupt, and again we will need to queue the data
Get data from UARTx_D (UARTx->D in with CMSIS)

## Slide 81: UART Control Register 1 (UART0_C1)
LOOPS: Enables loopback/single-pin (TX/RX) mode
DOZEEN: Doze enable – disable UART in sleep mode
RSRC: Selects between loopback and single-pin mode
M: Select 9-bit data mode (instead of 8-bit data)
WAKE: Wakeup method
ILT: Idle line type
PE: Parity enabled with 1
PT: Odd parity with 1, even parity with 0

## Slide 82: UART Control Register 2 (UART0_C2)
Interrupt Enables
  TIE: Interrupt when Transmit Data Register is empty
  TCIE: Interrupt when transmission completes
  RIE: Interrupt when receiver has data ready
Module Enables
  TE: Transmitter enable
  RE: Receiver enable
Other
  RWU: Put receiver in standby mode, will wake up when condition occurs
  SBK: Send a break character (all zeroes)

## Slide 83: UART Status Register 1 (UART_S1)
TDRE: Transmit data register empty, can write more data to data register
TC: Transmission complete.
RDRF: Receiver data register full, can read data from data register
IDLE: UART receive line has been idle for one full character time
OR: Receive overrun. Received data has overwritten previous data in receive buffer
NF: Noise flag. Receiver data bit samples don’t agree.
FE: Framing error. Received 0 for a stop bit, expected 1.
PF: Parity error. Incorrect parity received.

## Slide 84: UART Status Register 2 (UARTx_S2)
LBDIF: LIN break detect interrupt flag
RXEDGIF: Active edge on receive pin detected
MSBF: Send MSB first. Should be 0 for RS232
RXINV: Invert received signals (data, start, stop, etc.)
RWUID: Set idle bit upon wakeup?
BRK13: Set break character to 13 bits long (not 10)
LBKDE: LIN break character time.
RAF: Receiver is actively receiving data (not idle line)

## Slide 85: Software for Polled Serial Comm.
void Init_UART2(uint32_t baud_rate) {
uint32_t divisor;
// enable clock to UART and Port A
SIM->SCGC4 |= SIM_SCGC4_UART2_MASK;
SIM->SCGC5 |= SIM_SCGC5_PORTE_MASK;
// connect UART to pins for PTE22, PTE23
PORTE->PCR[22] = PORT_PCR_MUX(4);
PORTE->PCR[23] = PORT_PCR_MUX(4);
// ensure tx and rx are disabled before configuration
UART2->C2 &= ~(UARTLP_C2_TE_MASK | UARTLP_C2_RE_MASK);
// Set baud rate to 4800 baud
divisor = BUS_CLOCK/(baud_rate*16);
UART2->BDH = UART_BDH_SBR(divisor>>8);
UART2->BDL = UART_BDL_SBR(divisor);
// No parity, 8 bits, two stop bits, other settings;
UART2->C1 = UART2->S2 = UART2->C3 = 0;
// Enable transmitter and receiver
UART2->C2 = UART_C2_TE_MASK | UART_C2_RE_MASK;
}
Notes: This code initializes UART2 for polled communication. First the clocks are enabled for UART2 and PORTE (since UART2 uses the PORTE pins). Then the pin configuration registers are set so the muxes connect the UART to the pins for PTE22 and PTE23. Then the UART is configured as described and then enabled.

## Slide 86: Polled Serial Transmitter Code
void UART2_Transmit_Poll(uint8_t data) {
// wait until transmit data register is empty
while (!(UART2->S1 & UART_S1_TDRE_MASK))
;
UART2->D = data;
}
void main(void) {
char c;
// Initialization goes here
while (1) {
for (c='a'; c<='z'; c++) {
UART2_Transmit_Poll(c);
}
Notes: This code sends a byte of data, performing busy waiting as needed. The transmit function does not return until it has been able to send its byte.
The main function sends characters from a to z repeatedly as fast as possible.

## Slide 87: Polled Serial Receiver Code with Echo
uint8_t UART2_Receive_Poll(void) {
// wait until receive data register is full
while (!(UART2->S1 & UART_S1_RDRF_MASK))
;
return UART2->D;
}
void main(void) {
char c;
// Initialization goes here
while (1) {
c = UART2_Receive_Poll();
UART2_Transmit_Poll(c);
}
Notes: The receive function does not return until it has a byte. If no data is ever received, then the receive function will never return and the program will be stuck here.
The main function echoes back every character it receives

## Slide 88: Software for Interrupt-Driven Serial Comm.
Use interrupts
First, initialize peripheral to generate interrupts
Second, create single ISR with three sections corresponding to cause of interrupt
  Transmitter
  Receiver
  Error
Notes: Let’s look at using interrupts instead of polling. This will make the software much more modular and efficient, allowing the MCU to share its time among many tasks easily.

## Slide 89: Peripheral Initialization
void Init_UART2(uint32_t baud_rate) {
…
NVIC_SetPriority(UART2_IRQn, 2);
NVIC_ClearPendingIRQ(UART2_IRQn);
NVIC_EnableIRQ(UART2_IRQn);
UART2->C2 |= UART_C2_TIE_MASK |
UART_C2_RIE_MASK;
UART2->C2 |= UART_C2_RIE_MASK;
Q_Init(&TxQ);
Q_Init(&RxQ);
}
Notes: Here we add code to the Init_UART2 function to configure the NVIC and enable the UART to generate interrupts.

## Slide 90: Interrupt Handler: Transmitter
void UART2_IRQHandler(void) {
NVIC_ClearPendingIRQ(UART2_IRQn);
if (UART2->S1 & UART_S1_TDRE_MASK) {
// can send another character
if (!Q_Empty(&TxQ)) {
UART2->D = Q_Dequeue(&TxQ);
} else {
// queue is empty so disable tx
UART2->C2 &= ~UART_C2_TIE_MASK;
}
}
…
Notes: The UART IRQ Handler needs to check to see if a transmission completion caused the interrupt, in which case it needs either send the next data item or else stop transmitting.

## Slide 91: Interrupt Handler: Receiver
void UART2_IRQHandler(void) {
  …
if (UART2->S1 & UART_S1_RDRF_MASK) {
// received a character
if (!Q_Full(&RxQ)) {
Q_Enqueue(&RxQ, UART2->D);
} else {
// error - queue full.
while (1)
;
}
}
Notes: The UART IRQ handler also needs to check to see if a reception completion caused the interrupt, in which case the character should be removed from the UART and enqueued. If the queue is full then we have an error – in this case we freeze the system so the developer is sure to notice the problem.

## Slide 92: Interrupt Handler: Error Cases
void UART2_IRQHandler(void) {
…
if (UART2->S1 & (UART_S1_OR_MASK |
UART_S1_NF_MASK |
UART_S1_FE_MASK |
UART_S1_PF_MASK)) {
// handle the error
// clear the flag
}
}
Notes: The IRQ handler also needs to handle possible communication error cases (parity error, framing error, etc) – these responses will be situation dependent. These generally result from UART misconfiguration, noise on the incoming data, or not reading the data from the UART before the next data item arrives.

## Slide 93: Example UART Application
Many subsystems connect with the rest of the system using asynchronous serial communications
Lassen iQ GPS receiver module from Trimble
  Two full-duplex asynch. serial connections
  Three protocols supported
  Support higher speeds through reconfiguration

## Slide 94: USB to UART Interface
PCs haven’t had external asynchronous serial interfaces for a while, so how do we communicate with a UART?
USB to UART interface
  USB connection to PC
  Logic level (0-3.3V) to microcontroller’s UART (not RS232 voltage levels)
USB01A USB to serial adaptor
  http://www.pololu.com/catalog/product/391
  Can also supply 5 V, 3.3 V from USB

## Slide 95: Building on Asynchronous Comm.
Asynchronous communication is useful but runs into some problems when applying it to some applications
Problem #1
  Logic-level signals (0 to 1.65 V, 1.65 V to 3.3 V) are sensitive to noise and signal degradation
Problem #2
  Point-to-point topology does not support a large number of nodes well
    Need a dedicated wire to send information from one device to another
    Need a UART channel for each device the MCU needs to talk to
    Single transmitter, single receiver per data wire

## Slide 96: Solution to Noise: Higher Voltages
Use higher voltages to improve noise margin: +3 to +15 V, -3 to -15 V
Example IC (Maxim MAX3232) uses charge pumps to generate higher voltages from 3.3V supply rail

## Slide 97: Solution to Noise: Differential Signaling
Use differential signaling
  Send two signals: Buffered data (A), buffered complement of data (B)
  Receiver compares the two signals to determine if data is a one (A > B) or a zero (B > A)
Data into Transmitter
Data out of Transmitter, on bus
Data out of Receiver

## Slide 98: Solutions to Poor Scaling
Approaches
  Allow one transmitter to drive multiple receivers (multi-drop)
  Connect all transmitters and all receivers to same data line (multi-point network). Need to add a medium access control technique so all nodes can share the wire
Example Protocols
  RS-232: higher voltages, point-to-point
  RS-422: higher voltages, differential data transmission, multi-drop
  RS-485: higher voltages, multi-point

## Slide 99: Example Protocols
RS-232: higher voltages, point-to-point
RS-422: higher voltages, differential data transmission, multi-drop
RS-485: higher voltages, multi-point

## Slide 100: Protocol Comparison

## Slide 101: Factors to Consider
How fast can the data get through?
  Depends on raw bit rate, protocol overhead in packet
How many hardware signals do we need?
  May need clock line, chip select lines, etc.
How do we connect multiple devices (topology)?
  Dedicated link and hardware per device - point-to-point
  One bus for master transmit/slave receive, one bus for slave transmit/master receive
  All transmitters and receivers connected to same bus – multi-point
How do we address a target device?
  Discrete hardware signal (chip select line)
  Address embedded in packet, decoded internally by receiver
How do these factors change as we add more devices?

## Slide 102: Protocol Trade-Offs
Protocol | Speed | Signals Req. for Bidirectional Communication with N devices | Device Addressing | Topology
UART (Point to Point) | Fast – Tens of Mbit/s | 2*N (TxD, RxD) | None | Point-to-point full duplex
UART (Multi-drop) | Fast – Tens of Mbit/s | 2 (TxD, RxD) | Added by user in software | Multi-drop
SPI | Fast – Tens of Mbit/s | 3+N for SCLK, MOSI, MISO, and one SS per device | Hardware chip select signal per device | Multi-point full-duplex, multi-drop half-duplex buses
I2C | Moderate – 100 kbit/s, 400 kbit/s, 1 Mbit/s, 3.4 Mbit/s. Packet overhead. | 2: SCL, SDA | In packet | Multi-point half-duplex bus
Notes: Here we can see some trade-offs among the protocols. Which protocol is the best fit depends on the actual design’s constraints and goals, as well as whether there are peripherals which support the protocol.