## Slide 1: Using Direct Memory Access to Improve Performance

## Slide 2: Motivation
Performance improvements of moving work from software to hardware
  Speed: hardware faster than software
  Timing predictability:
    Makes less of system vulnerable to timing interference by software
    Reduces interference for other software
    Makes design and analysis easier

## Slide 3: Overview
Basic Concepts
DMA Peripherals in Cortex-M0+
DMA Applications
  Data Transfer
  Replacing ISRs

## Slide 4: Basic Concepts
Hardware which reads data from a source and writes it to a destination
  Can copy data quickly
  Can eliminate ISRs which just copy data (e.g. move ADC results into buffer)
Example: Data copy
  Source: source memory buffer
  Destination: destination memory buffer
  Trigger: software command
Various configurable options
  Number of data items to copy
  Source and destination addresses can be fixed or change (e.g. increment, decrement)
  Size of data item (1, 2, 4 bytes)
  When transfer starts
Operation
  Initialization: Configure controller
  Transfer: Data is copied
  Termination: Channel indicates transfer has completed

## Slide 5: More DMA Examples
Transmit data through UART
  Source: Memory buffer, address increments
  Destination: UART Transmit data buffer, address fixed
  Trigger: UART Transmit Complete
Save ADC samples in buffer
  Source: ADC result register, address fixed
  Destination: Memory buffer, address increments
  Trigger: ADC Conversion Complete
UART
ADC

## Slide 6: DMA and MCU Bus Architecture
Analog
Analog Comparator
12-bit DAC
Internal Voltage Reference
16-bit DAC
Timers
PWM
Low-Power Timer
Periodic Interrupt Timers
Real-Time Clock
HMI
GPIO
Touch-Sensing
Memories
Communications
I2C
SPI
UART
Flex IO
USB OTG
I2S
DMA Controller
ARM® Cortex®-M0+ Core
High-Speed System Bus
Bridge
Peripheral Bus
Ch 0
Ch 1
Ch 2
Ch 3

## Slide 7: DMA Controller Features
4 independent channels
  Channel 0 has highest priority
8-, 16- or 32-bit transfers, data size can differ between source and destination
Modulo addressability
  Pointer wraps around at end of buffer
  Enables ring buffers with size of 2N
Can trigger with hardware signal or software
How many data items are transferred per trigger?
  One: “Cycle stealing”
  All items: grabs bus
Hardware acknowledge/done signal

## Slide 8: DMA Controller Details

## Slide 9: DMA Controller
Notes: The DMA controller contains four channels. Each channel has various control and status registers (SAR, DAR, DSR, BCR, DCR). When a channel wants to perform a transfer it needs to arbitrate with other devices on the system bus to get permission. Once it gets permission, it is able to perform one or more transfer operations on the system bus.

## Slide 10: Address Registers
These registers determine from where the DMA will read its data, and to where it will write that data
DMA_SARn
  Source address register,
  Valid values 0 to 0x000f ffff
DMA_DARn
  Destination address register
  Valid values 0 to 0x000f ffff

## Slide 11: Byte Count Register
BCR: Bytes remaining to transfer
Decremented by 1, 2 or 4 after completing write (determined by destination data size)

## Slide 12: Status Register/Byte Count Register DMA_DSR_BCRn
Status flags: 1 indicates error
  CE: Configuration error
  BES: Bus error on source
  BED: Bus error on destination
  REQ: A transfer request is pending (more transfers to perform)
  BSY: DMA channel is busy
  DONE: Channel transfers have completed or an error occurred. Clear this bit in an ISR.

## Slide 13: DMA Control Register (DMA_DCRn)
EINT: Enable interrupt on transfer completion
ERQ: Enable peripheral request to start transfer
CS: Cycle steal
  0: Greedy - DMA makes continuous transfers until BCR == 0
  1: DMA shares bus, performs only one transfer per request
AA: Autoalign

## Slide 14: DMA Control Register (DMA_DCRn)
EADRQ – Enable asynchronous DMA requests when MCU is in Stop mode
SINC/DINC – Increment SAR/DAR by 1,2 or 4 based on size of data
SSIZE/DSIZE – Source/Destination data size.
  Don’t need to match – controller will perform extra reads or writes as needed (e.g. read one word, write two bytes).
  00: longword (32 bits)
  01: byte (8 bits)
  10: word (16 bits)
START – Write 1 to start transfer

## Slide 15: DMA Control Register (DMA_DCRn)
SMOD, DMOD – Source/Destination address modulo
  When non-zero, supports circular data buffer – address wraps around after 2n+3 bytes (16 bytes to 64 kilobytes)
  When zero, circular buffer is disabled
D_REQ: If 1, then when BCR reaches zero, channel will clear ERQ bit, preventing further hardware triggers of channel
LINKCC: Enables this channel to trigger another channel
  00: Disabled
  01: Two stages:
    Link to channel LCH1 after each cycle-steal transfer
    Link to channel LCH2 after BCR reaches 0
  10: Link to channel LCH1 after each cycle-steal transfer
  11: Link to channel LCH1 after BCR reaches 0
LCH1, LCH2: Values 00 to 11 specify linked DMA channel (0 to 3)

## Slide 16: Basic Use of DMA
Configuration
  Enable clock to DMA module (in SIM register SCGC7)
  Initialize control registers
  Load SARn with source address
  Load DARn with destination address
  Load BCRn with number of bytes to transfer
  Clear DSRn[DONE]
Transfer starts
  If ERQ is 1, hardware signal is asserted
  Or software sets DCRn[START]
Wait for end of transfer
  Interrupt generated if DCRn[EINT] is set (DMAn_IRQHandler)
  Or else poll DSRn[DONE]

## Slide 17: Demonstration: Memory Copy
Software-triggered
Could use as a fast version of memcpy function, but need to handle all cases
  Alignment of source and destination
  Detecting overlapping buffers
  Data size

## Slide 18: Triggering DMA Activity Using Peripherals
Can use trigger events from peripherals to start DMA transfer
Upon triggering, DMA can perform:
  One transfer (cycle steal mode)
  All transfers until BCR == 0 (continuous mode)
DMA Multiplexer (DMAMUX)
  Selects which source will trigger a DMA channel
Each DMA channel n has a configuration register DMAMUX_CHCFGn
  ENBL: Enable DMA channel
  TRIG: Enables triggering of DMA channel
  SOURCE: Selects triggering source
Notes: This is helpful because it eliminates an ISR, resulting in better system performance and less CPU loading.

## Slide 19: Trigger Sources
A variety of peripherals can trigger DMA activity
Trigger sources are chip-specific, so see KL25 Sub-Family Reference Manual (rev. 1), Chapter 3 - Chip Configuration, Section 3.4.8.1 DMA MUX Request Sources
Source # | Module | Description
0 | - | Disabled
2-7 | UART0,1, 2 | Receive, Transmit
16-19 | SPI0, 1 | Receive, Transmit
22-23 | I2C0, 1 | 
24-29 | TPM0 | Channels 0-5
32-35 | TPM1-2 | Channels 0-1
40 | ADC0 | 
42 | CMP0 | 
45 | DAC0 | 
49-53 | Port Control Module | Port A-E
54-56 | TPM0-2 | Overflow
57 | TSI | 
60-63 | DMAMUX | Always enabled

## Slide 20: Triggering DMA Transfers with PITs
DMA Channels 0, 1 can be triggered by PITs 0 and 1 as well as the previously listed sources
PIT generates a trigger pulse each time it reaches 0
  Disable interrupt for PITn by clearing TIE (interrupt enable) bit.
  Clear ENBL and TRIG bits in CHCFGn register
  Configure DMA Controller channel
  Configure timer
  Select trigger source with CHCFGn register and set ENBL and TRIG bits

## Slide 21: DAC Waveform Playback Example
Timer overflow ISR updates DAC
Timer overflow triggers DMA transfer to DAC

## Slide 22: DAC Waveform Playback Example
Timer overflow ISR updates DAC
Timer overflow triggers DMA transfer to DAC

## Slide 23: Configuration Details for DAC Playback
TPM0 expires when DAC update is needed
TPM Configuration
  Don’t enable timer interrupt
  TPM will still generate trigger event
When DMA is triggered by TPM:
  Copy one 16-bit data element from wave table (source) to DAC data register (DAC0->DAT[0])
  Increment source address, decrement byte count
When DMA finishes last transfer
  Generate interrupt
  IRQ handler will clear interrupt flags, restart DMA transfers
DMA Configuration
  Source, destination sizes = 2 bytes: SSIZE = DSIZE = 2
  Enable peripheral request: ERQ = 1
  Select hardware trigger
  One transfer per peripheral request, so use cycle-steal mode: CS = 1
  # Bytes to transfer: BCR = 2 bytes * # of samples
  Increment source register: SINC = 1
  Do not increment destination register: DINC = 0

## Slide 24: Performance Comparison
Traces
  Yellow: ISR is executing when trace is low
  Blue: DAC output (PTE30, pin 11 of J10)
Without DMA: Interrupt per sample
  4.7 microseconds per 620 microseconds
  0.758% of processor’s time
With DMA: Interrupt per cycle
  5.0 microseconds per 20 milliseconds
  0.025% of processor’s time
How is this useful?
  Saves CPU time
  Reduces timing vulnerability to interrupts being disabled
  Enables CPU to sleep longer, wake up less often (20 milliseconds vs. 620 microseconds)